## Slide 1: Time Frequency Analysis and Wavelet Transforms 時頻分析與小波轉換
授課者： 丁 建 均
Office：明達館723室, TEL： 33669652
E-mail: jjding@ntu.edu.tw
課程網頁：http://djj.ee.ntu.edu.tw/TFW.htm
歡迎大家來修課，也歡迎有問題時隨時聯絡！

## Slide 2
 評分方式：
平時分數: 15 scores
基本分12分，各位同學皆可拿到
另外再根據上課回答問題加分，每回答一次(無論答對否) 加 0.8 分
 本學期將另外規畫每位同學3題的非現場回答的問題
Homework: 60 scores
5 times, 每 3 週一次
請自己寫，和同學內容相同 ，將扣 60% 的分數，就算寫錯但好好寫也會給 40~95% 的分數，遲交分數打 8 折，不交不給分。
不知道如何寫，可用 E-mail 和我聯絡，或於下課時和老師討論
Term paper 25 scores

## Slide 3
Term paper 25 scores
方式有四種，可任選其中一種
(1) 書面報告
(10頁以上(不含封面)，中英文皆可，11或12的字體，題目可選擇和課程有關的任何一個主題。
格式和一般寫期刊論文或碩博士論文相同，包括 abstract, conclusion, 及 references，並且要分 sections，必要時有subsections。 References 的寫法, 可參照一般 IEEE 的論文的寫法 )
鼓勵多做實驗及模擬，有創新更好。
嚴禁剪刀漿糊 (Ctrl-C , Ctrl-V) 的情形，否則扣 60% 的分數
(2) Tutorial
限十二個名額，和書面報告格式相同，但 17頁以上(若為加強前人的 tutorial，則頁數為 (2/3)N + 12 以上，N 為前人 tutorial 之頁數)，題目由老師指定，以清楚且有系統的介紹一個主題的基本概念和應用為要求，為上課內容的進一步探討和補充，交Word 檔。
選擇這個項目的同學，學期成績加 3分

## Slide 4
(3) 口頭報告
限四個名額，每個人 40分鐘，題目可選擇和課程有關的任何一個主題。口頭報告將於 12月10日(第 12 週)進行。有意願的同學，請儘早告知，以先登記的同學為優先。
口頭報告時，鼓勵大家提問（包括口頭報告的同學，也可針對其他同學的報告內容提問）。曾經提問的同學，期末報告皆加 2 分。
選擇這個項目的同學，學期成績加 2分
(4) 編輯 Wikipedia
中文或英文網頁皆可，至少 2 個條目，但不可同一個條目翻成中文和英文。總計80行以上。限和課程相關者，自由發揮，越有條理、有系統的越好
選擇編輯 Wikipedia 的同學，請於明年1月7日(本學期最後一次上課)前，向我登記並告知我要編緝的條目(2 個以上)，若有和其他同學選擇相同條目的情形，則較晚向我登記的同學將更換要編緝的條目
編輯完成之後，要將連結寄給老師
書面報告、Tutorial、和編輯 Wikipedia，期限是 1月21日
以上若有做實驗模擬，請附上程式碼，會有額外的加分 (鼓勵不強制)

## Slide 5
上課方式
(1) 現場 (明達館231室)
(2) 錄影 ，影片將藉由 NTU Cool 下載
作業和報告繳交方式
http://cool.ntu.edu.tw
以下三種方式選擇一個
(1) 用 ceiba 來繳交作業電子檔 https://ceiba.ntu.edu.tw/
(2) 在課堂上交紙本作業
(3) 將作業放在明達館一樓丁建均教授的信箱
唯，作業程式碼一定要交電子檔 Tutorial 一定要交電子檔 (Word 或 Latex 原始碼) Wiki 要寄編輯條目的連結給老師

## Slide 6
上課時間：16 週
9/17,
9/24,
10/8, 出 HW1
10/15,
10/22, 交 HW1
10/29, 出 HW2
11/5,
11/12, 交 HW2
11/19, 出 HW3
11/26,
12/3, 交 HW3
12/10, Oral
12/17, 出 HW4
12/24,
12/31, 交 HW4,
1/7, 出 HW5
1/21, 交 HW5 及 term paper

## Slide 7
課程大綱：
(1) Introduction
(2) Short-Time Fourier Transform
(3) Gabor Transform
(4) Implementation of Time-Frequency Analysis
(5) Wigner Distribution Function
(6) Cohen’s Class Time-Frequency Distribution
(7) S Transforms, Gabor-Wigner Transforms, Matching Pursuit, and Other Time Frequency Analysis Methods
(8) Movement in the Time-Frequency Plane and Fractional Fourier Transforms
(9) Filter Design by Time-Frequency Analysis
(10) Modulation, Multiplexing, Sampling, and Other Applications
(續)

## Slide 8
課程大綱：
(11) Hilbert Huang Transform
(12) From Haar Transforms to Wavelet Transforms
(13) Continuous Wavelet Transforms
(14) Continuous Wavelet Transforms with Discrete Coefficients
(15) Discrete Wavelet Transform
(16) Applications of the Wavelet Transform

## Slide 9
上課資料：
(1) 講義 (將放在網頁上，請大家每次上課前先印好)
(2) S. Mallat, A Wavelet Tour of Signal Processing: The Sparse Way, Academic Press, 3rd ed., 2009.
(3) S. Qian and D. Chen, Joint Time-Frequency Analysis: Methods and
Applications, Prentice-Hall, 1996.
(4) P. Flandrin, Time-frequency / Time Scale Analysis, translated by J. Stöckler, Academic Press, San Diego, 1999.
(5) K. Grochenig, Foundations of Time-Frequency Analysis, Birkhauser, Boston, 2001.
(6) L. Debnath, Wavelet Transforms and Time-Frequency Signal Analysis, Birkhäuser, Boston, 2001.
(7) F. Hlawatsch and F. Auger, Time-frequency Analysis Concepts and Methods, Wiley, London, 2008.

## Slide 10
Matlab Program
Download: 請洽台大各系所
參考書目
洪維恩，Matlab 程式設計，旗標，台北市，2013 . (合適的入門書)
張智星，Matlab 程式設計入門篇，第四版，碁峰，2016.
蒙以正，數位信號處理：應用 Matlab，旗標，台北市，2007.
繆紹綱譯，數位影像處理 - 運用 Matlab，東華，2005.
預計看書學習所花時間： 3~5 天
Python Program
Download: https://www.python.org/

## Slide 11
Tutorial 可供選擇的題目(可以略做修改)
(1) Window Size Selection for the Short-Time Fourier Transform
(2) Seismic Wave Analysis Using Time-frequency Analysis
(3) Sparse Coding Using Compressive Sensing
(4) Recent Development of Time-Frequency Reassignment
(5) Synchrosqueezing Transform
(6) Haar-Like Features for Object Identification
(7) Dual Tree Complex Wavelet Transforms
(8) Prediction Techniques Using Hilbert-Huang Transforms
(9) Prediction Techniques Using Wavelet Transforms
(10) Wavelet Neural Network
(11) Fresnelet
(12) Shearlet
有加 * 號的是學長寫過的，但鼓勵同學再加強

## Slide 12: I. Introduction
Fourier transform (FT)
Time-Domain  Frequency Domain
↑ t varies from ∞~∞
Laplace Transform
Cosine Transform, Sine Transform, Z Transform.
Some things make these operations not practical:
Only the case where t0  t  t1 is interested.
(2) Not all the signals are suitable for analyzing in the frequency domain.
It is hard to observe the variation of spectrum with time by these operations

## Slide 13
Example 1: x(t) = cos(440 t) when t < 0.5,
x(t) = cos(660 t) when 0.5  t < 1,
x(t) = cos(524 t) when t  1
The Fourier transform of x(t)
Frequency

## Slide 14
Finite-Supporting Fourier Transform
Short-Time Fourier Transform (STFT)
w(t): window function 或 mask function
STFT 也稱作 windowed Fourier transform 或
time-dependent Fourier transform
[Ref] L. Cohen, Time-Frequency Analysis, Prentice-Hall, New York, 1995.
[Ref] A. V. Oppenheim and R. W. Schafer, Discrete-Time Signal Processing,
London: Prentice-Hall, 3rd ed., 2010.

## Slide 15
最簡單的例子： w(t) = 1 for |t|  B,
w(t) = 0 otherwise
此時 Short-time Fourier transform 可以改寫
其他的例子：
一般我們把 exp(- σt2) 稱作為 Gaussian function 或 Gabor function
此時的 Short-Time Fourier Transform 亦稱作 Gabor Transform
-B B
t-axis
t-axis
0
0

## Slide 16
(C) Gabor Transform
S. Qian and D. Chen, Joint Time-Frequency Analysis: Methods and Applications,
Prentice Hall, N.J., 1996.
R. L. Allen and D. W. Mills, Signal Analysis: Time, Frequency, Scale, and
Structure, Wiley- Interscience.
Common Features for short-time Fourier transforms and Gabor transforms
(1) The instantaneous frequency can be observed
(2) Without Cross Term
(3) Poor clarity

## Slide 17
Example: x(t) = cos(440 t) when t < 0.5,
x(t) = cos(660 t) when 0.5  t < 1,
x(t) = cos(524 t) when t  1
The Gabor transform of x(t) ( = 200)
用 Gray level 來表示 X(t, f) 的 amplitude
t–axis (Second)
f -axis (Hertz)

## Slide 18
Instantaneous Frequency 瞬時頻率
If
then the instantaneous frequency of x(t) at t0 are
If the order of
> 1, then instantaneous frequency varies with time
(以頻率 frequency 表示)
(以角頻率 angular frequency 表示)：
around t0

## Slide 19
Frequency Modulation
Music
Speech
Others (Animal voice, Doppler effect, seismic waves, radar system, optics, rectangular function)
自然界中，頻率會隨著時間而改變的例子
In fact, in addition to sinusoid-like functions, the instantaneous frequencies of other functions will inevitably vary with time.

## Slide 20
Sinusoid Function
Chirp function
Instantaneous frequency =
acoustics, wireless communication, radar system, optics
例： ㄚ (F1 = 900Hz, F2 = 1200Hz) , ㄧ (F1 = 300Hz, F2 = 2300Hz)
F1 由嘴唇的大小決定, F2 - F1 由如面的高低決定
Higher order exponential function

## Slide 21
Example 2
(1) t  [0, 3]
(2) t  [0, 3]

## Slide 22
Fourier transform
f (Hz)
f (Hz)

## Slide 23
(1)
(2)

## Slide 24
left: x1(t) = 1 for |t|  6, x1(t) = 0 otherwise, right: x2(t) = cos(6t  0.05t2)
Gabor transform
 -axis
t -axis
Example 3

## Slide 25
Example 4
Data source: http://oalib.hlsresearch.com/Whales/index.html

## Slide 26: Why Time-Frequency Analysis is Important?
Many digital signal processing applications are related to the spectrum or the bandwidth of a signal.
If the spectrum and the bandwidth can be determined adaptive, the performance can be improved.
 modulation,  signal identification,
 multiplexing,  acoustics,
 filter design,  system modeling,
 data compression,  radar system analysis
 signal analysis,  sampling

## Slide 27
Example: Generalization for sampling theory
假設有一個信號，
 The supporting of x(t) is t1  t  t1 + T, x(t)  0 otherwise
 The supporting of X( f )  0 is -B  f  B, X( f )  0 otherwise
根據取樣定理， t  1/F , F =2B, B:頻寬
所以，取樣點數 N 的範圍是
N = T/t  TF
重要定理：一個信號所需要的取樣點數的下限，等於它時頻分佈的面積
f
t
B
-B
t1
t1+T

## Slide 28
Q2: How to use time-frequency analysis to reduce the number of sampling points?
Time-frequency analysis is an efficient tool for adaptive signal processing.
Q1：Scaling 對於一個信號的取樣點數有沒有影響？
Hint:

## Slide 29
(1) Short-time Fourier transform (STFT)
(rec-STFT, Gabor, …)
square
spectrogram
improve
S transform
(2) Wigner distribution function (WDF)
combine
Gabor-Wigner Transform
improve
windowed WDF
improve
Cohen’s Class Distribution
(Choi-Williams, Cone-Shape, Page, Levin, Kirkwood, Born-Jordan, …)
improve
Pseudo L-Wigner Distribution
(4) Time-Variant Basis Expansion
Matching Pursuit and Compressive Sensing
Prolate Spheroidal Wave Function
(5) Hilbert-Huang Transform
(3) Wavelet transform
Haar and Daubechies
Coiflet, Morlet
Directional Wavelet Transform
(唯一跳脫 Fourier transform 的架構)
Asymmetric STFT
generalized spectrogram
improve
Polynomial Wigner Distribution
時頻分析大家族

## Slide 30
 Continuous Wavelet Transform
forward wavelet transform:
(t): mother wavelet, a: location, b: scaling,
inverse wavelet transform:
a,b(t) is dual orthogonal to (t).
 | output
Fourier transform | X(f), f: frequency
time-frequency analysis | X(t, f), t: time, f: frequency
wavelet transform | X(a, b), a: time, b: scaling

## Slide 31
限制：
(1) when a1 = a and b1 = b,
otherwise
(2) (t) has a finite time interval
Two parameters, a: 調整位置, b: 調整寬度
應用： adaptive signal analysis
思考：需要較高解析度的地方，b 的值應該如何？

## Slide 32
Wavelet 的種類甚多
Mexican hat wavelet, Haar Wavelet, Daubechies wavelet, triangular wavelet, …………
例子： Mexican hat wavelet 隨 a and b 變化之情形
a = 2, b = 1
a = 6, b = 1
a = 10, b = 1
a = 6, b = 0.5
a = 6, b = 2
a = 6, b = 3

## Slide 33
 Discrete Wavelet Transform (DWT)
The discrete wavelet transform is very different from the continuous wavelet transform. It is simpler and more useful than the continuous one.
x1,L[n]
x1,H[n]
g[n]
x[n]
h[n]
 2
 2
x[n] 的低頻成份
x[n] 的高頻成份
lowpass filter
highpass filter
down sampling
xL[n]
xH[n]
down sampling
N-points
L-points
L-points

## Slide 34
例子：2-point Haar wavelet
g[n] = 1/2 for n = −1, 0
g[n] = 0 otherwise
h[0] = 1/2, h[−1] = −1/2,
h[n] = 0 otherwise
n
g[n]
-3 -2 -1 0 1 2 3
½ ½
n
h[n]
-3 -2 -1 0 1 2 3
½
-½
then
(兩點平均)
(兩點之差)

## Slide 35
一般的 wavelet, g[n] 和 h[n] 點數會多於 2 點
但是 g[n] 通常都是 lowpass filter 的型態
h[n] 通常都是 highpass filter 的型態
Discrete wavelet transform 有很多種
(discrete Haar wavelet, discrete Daubechies wavelet, B-spline DWT, symlet, coilet, ……..)

## Slide 36
x[m, n]
g[n]
h[n]
 2
 2
along n
along n
v1,L[m, n]
v1,H[m, n]
g[m]
h[m]
along m
 2
x1,L[m, n]
 2
along m
x1,H1[m, n]
g[m]
h[m]
along m
along m
 2
 2
x1,H2[m, n]
x1,H3[m, n]
2-D 的情形
m 低頻, n 低頻
m 高頻, n 低頻
m 低頻, n 高頻
m 高頻, n 高頻
L-points
L-points
M ×N
n
m
x[m, n]

## Slide 37
原影像
Pepper.bmp
2-D DWT
的結果
x1,L[m, n]
x1,H1[m, n]
x1,H2[m, n]
x1,H3[m, n]

## Slide 38
3次2-D DWT的結果

## Slide 39
應用： 影像壓縮 (JPEG 2000)
其他應用：edge detection
corner detection
filter design
pattern recognition
music signal processing
economical data
temperature analysis
feature extraction
biomedical signal processing

## Slide 40: 附錄一：聲音檔的處理 (by Matlab)
電腦中，沒有經過壓縮的聲音檔都是 *.wav 的型態
讀取： audioread
例： [x, fs] = audioread('C:\WINDOWS\Media\ringin.wav');
可以將 ringin.wav 以數字向量 x 來呈現。 fs: sampling frequency
這個例子當中 size(x) = 9981 1 fs = 11025
思考: 所以，取樣間隔多大?
這個聲音檔有多少秒？
A. 讀取聲音檔
一個聲音檔如果太大，我們也可以只讀取它部分的點
[x, fs]=audioread('C:\WINDOWS\Media\ringin.wav', [4001 5000]);
% 讀取第4001至5000點

## Slide 41
畫出聲音的波型
time = [0:length(x)-1]/fs; % x 是前頁用 wavread 所讀出的向量
plot(time, x)
注意： *.wav 檔中所讀取的資料，值都在 1 和 +1 之間

## Slide 42
有些聲音檔是 雙聲道 （Stereo）的型態 (俗稱立體聲)
例： [x, fs]=audioread('C:\WINDOWS\Media\notify.wav');
size(x) = 29823 2 fs = 22050

## Slide 43
X = fft(x); plot(abs(X)*dt); % dt = 1/fs
fft 橫軸 轉換的方法
(1) Using normalized frequency F: F = m / N.
(2) Using frequency f, f = F  fs = m  (fs / N).
B. 繪出頻譜
abs(X)*dt
m
ringin.wav 的頻譜

## Slide 44
abs(X)*dt
ringin.wav 的頻譜
F
f
abs(X)*dt
ringin.wav 的頻譜

## Slide 45
C. 聲音的播放
(1) audioplay(x): 將 x 以 11025Hz 的頻率播放
(時間間隔 = 1/11025 = 9.07  105 秒)
(2) sound(x): 將 x 以 8192Hz 的頻率播放
(3) sound(x, fs) 或 sound(x, fs) 或 audioplay(x , fs):
將 x 以 fs Hz 的頻率播放
Note: (1)~(3) 中 x 必需是1 個column (或2個 columns)，且 x 的值應該 介於 1 和 +1 之間
(4) soundsc(x, fs): 自動把 x 的值調到 1 和 +1 之間 再播放

## Slide 46
audiowrite(x, fs, waveFile)
將數據 x 變成一個 *.wav 檔，取樣速率為 fs Hz
 x 必需是1 個column (或2個 columns)  x 值應該 介於 1 和 +1 之間
 若沒有設定fs，則預設的fs 為 8000Hz
D. 用 Matlab 製作音檔： audiowrite

## Slide 47
E. 用 Matlab 錄音的方法
錄音之前，要先將電腦接上麥克風，且確定電腦有音效卡
(部分的 notebooks 不需裝麥克風即可錄音)
範例程式：
Sec = 3;
Fs = 8000;
recorder = audiorecorder(Fs, 16, 1);
recordblocking(recorder, Sec);
audioarray = getaudiodata(recorder);
執行以上的程式，即可錄音。
錄音的時間為三秒，sampling frequency 為 8000 Hz
錄音結果為 audioarray，是一個 column vector (如果是雙聲道，則是兩個 column vectors)

## Slide 48
audioplay(audioarray, Fs); % 播放錄音的結果
t = [0:length(audioarray)-1]./Fs;
plot (t, audioarray‘); % 將錄音的結果用圖畫出來
xlabel('sec','FontSize',16);
audiowrite(audioarray, Fs, ‘test.wav’) % 將錄音的結果存成 *.wav 檔
範例程式 (續)：

## Slide 49
recordblocking(recorder, Sec);
(錄音的指令)
recorder: the parameters obtained by the command “audiorecorder”
Sec: the time length for recording
audioarray = getaudiodata(recorder);
(將錄音的結果，變成 audioarray 這個 column vector，如果是雙聲道，則 audioarray 是兩個 column vectors)
以上這三個指令，要並用，才可以錄音
指令說明：
recorder = audiorecorder(Fs, nb, nch);
Fs: sampling frequency,
nb: using nb bits to record each data
nch: number of channels (1 or 2)
(提供錄音相關的參數)