## Slide 1
XIV. Discrete Wavelet Transform
(1) discrete input to discrete output
(3) 忽略了 scaling function 和 mother wavelet function 的分析
但是保留了階層式的架構
14.1 概念
(2) 由 continuous wavelet transform with discrete coefficients 演變而來的， (比較 page 387) 但是大幅簡化了其中的數學

## Slide 2
x[n]
g[n]
h[n]
 2
 2
x1,L[n]
x1,H[n]
 2
: downsampling by the factor of 2
 Q
x[n]
z[n]
14.2 1-D Discrete Wavelet Transform
lowpass filter
highpass filter
input
N-points
L-points
L-points

## Slide 3
x[n]
輸入：
(不需算 ，
直接以 x[n] 作為 initial
Low pass filter g[n]
High pass filter h[n]
1st stage
角色似 scaling function
角色似 wavelet function
(相當於 page 387 的 gn)
(相當於 page 387 的 hn)

## Slide 4
further decomposition (from the (a−1)th stage to the ath stage)
x1,L[n]
x1,H[n]
g[n]
x[n]
h[n]
 2
 2
g[n]
h[n]
 2
 2
x2,L[n]
x2,H[n]

## Slide 5
(1) 有的時候，對於 也再作細分
xa,H[n]
(2) 若 input 的 x[n] 的 length 為N,
則 ath stage xa,L[n], xa,H[n] 的 length 為N/2a
(3) 經過 DWT 之後，全部點數仍接近 N 點

## Slide 6
(4) 以頻譜來看
X1,L(f)
X1,H(f)
X1,H(f)
X2,H(f)
X2,L(f)
X1,H(f)
X2,H(f)
X3,H(f)
X3,L(f)
f-axis
f-axis
f-axis

## Slide 7
x[m, n]
g[n]
h[n]
 2
 2
along n
along n
v1,L[m, n]
v1,H[m, n]
g[m]
h[m]
along m
 2
x1,L[m, n]
 2
along m
x1,H1[m, n]
g[m]
h[m]
along m
along m
 2
 2
x1,H2[m, n]
x1,H3[m, n]
14.3 2-D Discrete Wavelet Transform

## Slide 8
輸入：
x[m, n]
Low pass filter g[n]
High pass filter h[n]
 along n
 along m

## Slide 9
from R. C. Gonzalez and R. E. Woods, Digital Image Processing, Chap. 7, 2nd edition, Prentice Hall, New Jersey, 2002.
原圖：正方形
x1,H3[m, n]
m
n
x2,H3[m, n]
x3,H3

## Slide 10
from R. C. Gonzalez and R. E. Woods, Digital Image Processing, Chap. 7, 2nd edition, Prentice Hall, New Jersey, 2002.
原圖：Lena

## Slide 11
保留 x1,L[m, n]，捨棄其他部分
 compression & noise removing
 (directional) edge detection
保留 x1,H1[m, n]
捨棄其他部分
或保留 x1,H2[m, n]
 x1,H3[m, n] 當中所包含的資訊較少
corner detection?

## Slide 12
14.4 Complexity of the DWT
x[n]  y[n], length(x[n]) = N, length(y[n]) = L,
(1) Complexity of the 1-D DWT (without sectioned convolution)
(N+L1)-point discrete Fourier transform (DFT)
(N+L1)-point inverse discrete Fourier transform (IDFT)

## Slide 13
(2) 當 N >>> L 時，使用 “sectioned convolution” 的技巧
x[n]
將 x[n] 切成很多段，每段長度為 N1
總共有 段
(N > N1 >> L)
n
N1
N1
x1[n]
x2[n]
x3[n]
xS[n]

## Slide 14
 重要概念：
The complexity of the 1-D DWT is linear with N
when N >>> L
complexity:

## Slide 15
(3) Multiple stages 的情形下
Complexity 近似於:
 若 xa,H[n] 不再分解
 若 xa,H[n] 也細分
Complexity 近似於:
(和 DFT 相近)

## Slide 16
(4) Complexity of the 2-D DWT on page 431 (without sectioned convolution )
The first part needs M 1-D DWTs and the input for each 1-D DWT has N points
The second part needs N+L1 1-D DWTs and the input for each 1-D DWT has M points

## Slide 17
(5) Complexity of the 2-D DWT (with Sectioned Convolution)
Image
The original size: M  N
The size of each part: M1  N1
 重要概念：
If the method of the sectioned convolution is applied,
the complexity of the 2-D DWT is linear with MN.

## Slide 18
(6) Multiple stages, two dimension
x[m, n] 的 size 為 M × N
total complexity
 若 xa,H1[n], xa,H2[n], xa,H3[n] 不細分，只細分 xa,L[n]
 若 xa,H1[n], xa,H2[n], xa,H3[n] 也細分
total complexity

## Slide 19
14.5 Many Operations Also Have Linear Complexities
事實上，不只 wavelet 有 linear complexity
當 input 和 filter 長度或大小相差懸殊時
1-D convolution 的 complexity 是 linear with N.
2-D convolution 的 complexity 是 linear with MN.
(和傳統 Nlog2N, MNlog2(MN) 的觀念不同）
很重要的概念

## Slide 20
 Note：DCT 的 complexity 也是 linear with MN
(divided into 8 × 8 blocks)
complexity :

## Slide 21
x[n]
g[n]
h[n]
x1,L[n]
x1,H[n]
 2
 2
analysis
synthesis
 2
 2
g1[n]
h1[n]
x0[n]
 2
: upsampling by the factor of 2
 Q
a[n]
b[n]
for r = 1, 2, Q−1
14.6 Reconstruction
g1[n], h1[n] 要滿足什麼條件，才可以使得 x0[n] = x[n]？

## Slide 22
 If a[n] = b[2n],
 If a[2n] = b[n],
a[2n+1] = 0
(Proof):
Z transform
↓ 2 (downsampling)
↑ 2 (upsampling)
用 Z transform 來分析
Reconstruction Problem

## Slide 23
Perfect reconstruction:

## Slide 24
Perfect reconstruction:
條件：
where

## Slide 25
14.7 Reconstruction 的等效條件
if and only if
這四個條件被稱作
biorthogonal conditions

## Slide 26
Note: (a)
(b) 令
(Proof)
From
Therefore,
inverse Z transform

## Slide 27
orthogonality 條件 1
(c) Similarly, substitute
into
orthogonality 條件 2
after the process the same as that of the above

## Slide 28
(d) Since
(e) 同理
orthogonality 條件 3
orthogonality 條件 4

## Slide 29
 Finite length
為了 implementation 速度的考量
g[n]  0 only when L  n  L
h[n]  0 only when L  n  L
h1[n] , g1[n] ?
令
則根據 page 448,
14.8 DWT 設計上的條件
 Reconstruction
複習:

## Slide 30
 Lowpass-highpass pair
 因為
k 必需為 odd

## Slide 31
(1)
(2)
g[n]  0 only when 0  n  L1
h[n]  0 only when 0  n  L1
(3)
k 必需為 odd
(4)
g[n] 為 lowpass filter
h[n] 為 highpass filter
第三個條件較難達成，是設計的核心
(for reconstruction)
(h[n], g[n] have finite lengths)
(h1[n], g1[n] have finite lengths)
(lowpass and highpass pair)
14.9 整理：DWT 的四大條件

## Slide 32
14.10 Two Types of Perfect Reconstruction Filters
(1) QMF (quadrature mirror filter)
k is odd
g[n] has finite length

## Slide 33
(2) Orthonormal
k is odd
g1[n] has finite length

## Slide 34
大部分的 wavelet 屬於 orthonormal wavelet
文獻上，有時會出現另一種 perfect reconstruction filter, 稱作
CQF (conjugate quadrature filter)
然而，CQF 本質上和 orthonormal filter 相同

## Slide 35
 discrete Haar wavelet (最簡單的)
otherwise
otherwise
otherwise
otherwise
14.11 Several Types of Discrete Wavelets
是一種 orthonormal filter

## Slide 36
 discrete Daubechies wavelet (8-point case)
n = 0 ~ 7
otherwise
n = −7 ~ 0
otherwise
n = 0 ~ 7
otherwise
n = −7 ~ 0
otherwise

## Slide 37
 discrete Daubechies wavelet (4-point case)
 discrete Daubechies wavelet (6-point case)
 discrete Daubechies wavelet (10-point case)
 discrete Daubechies wavelet (12-point case)

## Slide 38
symlet (6-point case)
symlet (8-point case)
symlet (10-point case)
Daubechies wavelets and symlets are defined for N is a multiple of 2

## Slide 39
coiflet (12-point case)
The Daubechies wavelet, the symlet, and the coiflet are all orthonormal filters.
Coiflets are defined for N is a multiple of 6
coiflet (6-point case)

## Slide 40
The Daubechies wavelet, the symlet, and the coiflet are all derived from the “continuous wavelet with discrete coefficients” case.
Physical meanings:
Daubechies wavelet
Symlet
Coilfet
The ? point Daubechies wavelet has the vanish moment of p.
The vanish moment is the same as that of the Daubechies wavelet, but the filter is more symmetric.
The scaling function also has the vanish moment.
for 1 ≦ k ≦ p
The ? point coiflet has the vanish moment of p.

## Slide 41
Step 1
Q: 如何用 Matlab 寫出
Step 2
Hint: 在 Matlab 當中，可以用 [-.25, .5, -.25] 自己和自己 convolution k-1 次算出來
Step 3 算出 zkP1(z) 的根 (i.e., zkP1(z) = 0 的地方)
Q: 在 Matlab 當中應該用什麼指令
(When p = 2, P(y) = 2y + 1)
(When p = 2, P1(z) = 2 – 0.5z – 0.5z -1)
(When p = 2, roots = 3.7321, 0.2679)
14.12 產生 Discrete Daubechies Wavelet 的流程

## Slide 42
Step 4 算出
z1, z2, …, zp-1 為 zkP1(z) 當中，絕對值小於 1 的 roots
Step 5 算出
注意： Z transform 的定義為
所以 coefficients 要做 reverse
(When p = 2, g0[n] = [1 1.7321 0.4641 -0.2679])
n = -3 ~ 0

## Slide 43
Step 7 Time reverse
Step 6 Normalization
(When p = 2, g1[n] = [0.4830 0.8365 0.2241 -0.1294])
n = -3 ~ 0
Then, the (2p)-point discrete Daubechies wavelet transform can be obtained

## Slide 44
14.13 2x2 Structure Form and the Lifting Scheme
x[n]
g[n]
h[n]
x1,L[n]
x1,H[n]
 2
 2
can be changed into the following 2x2 structure
Z-1 means delayed by 1
ge[n] = g[2n]
go[n] = g[2n+1]
he[n] = h[2n]
ho[n] = h[2n+1]
where
x[n]
 2
Z-1
 2
ge[n]
he[n]
go[n]
ho[n]
x1,L[n]
x1,H[n]
xe[n]
xo[n]
The analysis part

## Slide 45
(Proof): From page 427,
where
Z-1
 2
x[n]
x[2n-1]
Similarly,

## Slide 46
Original Structure:
Two Convolutions of an N-length input and an L-length filter
New Structure:
Four Convolutions of an (N/2)-length input and an (L/2)-length filter, which is more efficient. (Why?)

## Slide 47
x1,L[n]
x1,H[n]
 2
 2
g1[n]
h1[n]
x0[n]
Similarly, the synthesis part
can be changed into the following 2x2 structure
x1,L[n]
x1,H[n]
g1,e[n]
g1,o[n]
h1,e[n]
h1,o[n]
Z-1
 2
 2
x0[n]
g1,e[n] = g1 [2n]
g1,o[n] = g1 [2n+1]
where
h1,e[n] = h1 [2n]
h1,o[n] = h1 [2n+1]

## Slide 48
Lifting Scheme:
Reversible After Quantization
x[n]
Q(g[n])
Q(h[n])
x1,L[n]
x1,H[n]
 2
 2
 2
 2
Q(g1[n])
Q(h1[n])
x0[n]
 x[n]
Q( ) means quantization (rounding, flooring, ceiling ……)
After performing quantization, the DWT may not be perfectly reversible
14.14 Lifting Scheme

## Slide 49
From page 468
Since
then
from page 455 one set that

## Slide 50
where
Then can be decomposed into
Then the DWT can be approximated by
where T1(z)  L1(z), T2(z)  L2(z), T3(z)  L3(z)

## Slide 51
x[n]
 2
Z-1
 2
x1,H[n]
xe[n]
xo[n]
t3[n]
t2[n]
t1[n]
Z-m
x1,L[n]
Lifting Scheme
The Z transforms of t1[n], t2[n], and t3[n] are T1(z), T2(z), and T3(z), respectively.
analysis part

## Slide 52
Lifting Scheme
synthesis part
x1,L[n]
x1,H[n]
Z
 2
 2
x0[n–m]
-t1[n]
-t2[n]
-t3[n]
Zm

## Slide 53
If one perform quantization for t1[n], t2[n], and t3[n], then the discrete wavelet transform is still reversible.
W. Sweldens, “The lifting scheme: a construction of second generation wavelets,”
Applied Comput. Harmon. Anal., vol. 3, no. 2, pp. 186-200, 1996.
I. Daubechies and W. Sweldens, “Factoring wavelet transforms into lifting steps,”
J. Fourier Anal. Applicat., vol. 4, pp. 246-269. 1998.

## Slide 54
附錄十四 誤差計算的標準
若原來的信號是 x[m, n]，要計算 y[m, n] 和 x[m, n] 之間的誤差，有下列幾種常見的標準
(3) error norm (i.e., Euclidean distance)
(2) square error
(1) maximal error
(4) mean square error (MSE)，信號處理和影像處理常用

## Slide 55
(5) root mean square error (RMSE)
(6) normalized mean square error (NMSE)
(7) normalized root mean square error (NRMSE)， 信號處理和影像處理常用

## Slide 56
(8) signal to noise ratio (SNR)，信號處理常用
(9) peak signal to noise ratio (PSNR)，影像處理常用
XMax: the maximal possible value of x[m, n]
In image processing, XMax = 255
for color image:
color = R, G, or B

## Slide 57
(10) structural dissimilarity (DSSIM)
有鑑於 MSE 和 PSNR 無法完全反應人類視覺上所感受的誤差，在 2004 年被提出來的新的誤差測量方法
Z. Wang, A. C. Bovik, H. R. Sheikh, and E. P. Simoncelli, “Image quality assessment: from error visibility to structural similarity,” IEEE Trans. Image Processing, vol. 13, no. 4, pp. 600−612, Apr. 2004.
x, y: means of x and y
x2, y2: variances of x and y
xy: covariance of x and y
c1, c2: adjustable constants
L: the maximal possible value of x  the minimal possible value of x