## Slide 1
XV. Applications of Wavelet Transforms
Wavelet 所適用的 applications，通常有以下兩大特點：
(1) 信號的頻率分佈，會隨著不同的時間(或地點)有較大變異
(2) Multiscale 的分析扮演重要的角色
Larger sampling interval  ignoring the detail
Smaller sampling interval  requiring a lot of data
Wavelet transforms compromise them.
目前，文獻上，80% 以上的應用和 image processing 有關

## Slide 2
JPEG 2000 架構
Image
RGB to YCbCr
4:2:0
Discrete Wavelet Transform
Quantization
Bit Plane Conversion
Fractional
Bit-plane coding
(Tier 1)
Binary arithmetic coding
Tier 2 Encoder
JPEG 2000 file
Quantization Table
檔頭
註：感謝 2010年修課的潘冠臣同學幫忙整理
Tier 1: zero coding, sign coding, magnitude refinement coding, run length coding
Tier 2: 用以控制檔案大小 (例如只取比較重要的地方編碼)
(1) Image Compression (JPEG 2000)

## Slide 3
The subbands of the discrete wavelet transform (DWT)

## Slide 4
比較：傳統 JPEG 架構
8 × 8
4:2:0
DCT
量子化
量子化表
AC係數
Zigzag Scan
DC係數
差分 編碼
Huffman Coding
Huffman Coding
JPEG file
檔頭
Image
問題：由於 8  8 的切割，在高壓縮率時會造成 blocking effect
RGB to YCbCr

## Slide 5
Original image
DCT-based image compression
Wavelet-based image compression
CR = 53.4333
CR = 51.3806
註：感謝 2006年修課的黃俊德同學
CR: compression ratio

## Slide 6
bpp: bit per pixel (每一點平均需要多少個 bits)
PSNR: peak signal to noise ratio (PSNR), see page 480

## Slide 7
使用 JPEG 2000 做影像壓縮的優點：
所以，在高壓縮率之下，重建的影像仍有不錯的品質
Question:
Why JPEG 2000 has not replaced the status of JPEG now?
C. Christopoulos, A. Skodras, and T. Ebrahimi, “The JPEG2000 still image coding system: An overview,” IEEE Trans. Consumer Electronics, vol. 46, no. 4, pp.1103-1127, Nov. 2000.
參考資料
(1)
(2)
(3)

## Slide 8
B.J. Kim, Z. Xiong, and W.A. Pearlman. “Low bit-rate scalable video coding with 3-D set partitioning in hierarchical trees (3-D SPIHT),” IEEE Trans. Circuits Syst. Video Technol., vol. 10, pp. 1374-1387, 2000.
Another Compression Algorithm: SPIHT
Using the correlation among high frequency parts in different layers

## Slide 9
(2) Edge and Corner Detection
(3) Pattern recognition
(4) 強調前景，壓縮背景
(a) Feature extraction
(Using the wavelet features)
(b) Computation Time 和縮小的 pattern 互相比較 (節省運算)

## Slide 10
(5) Filter Design
如何不傷到 edge，又能夠將 noise 去除掉？

## Slide 11
x[n]
g[n]
h[n]
x1,L[n]
x1,H[n]
 2
 2
analysis
synthesis
 2
 2
h1[n]
g1[n]
x0[n]
a1[n]
做 filter design 時，可以令
a1[n] = 1,
a2[n] = 0 for non-edge region
a2[n] = 1 for edge region
a2[n]
One-stage wavelet filter
必要時可使用 two-stage 以上的 wavelet filter
以 x1,H[n] 的 amplitude 來區分

## Slide 12
x2,L[n]
x2,H[n]
x1,H[n]
(2nd stage, lowpass)
(2nd stage, highpass)
(1st stage, highpass)

## Slide 13
原信號
使用one-stage 的 wavelet filter
使用two-stage 的 wavelet filter

## Slide 14
(6) Music
音樂當中，音每高一個音階，頻率就增為二倍
(7) Acoustics
音樂 每一音階有12個半音，增加一個半音，頻率增加 21/12 倍
(等比級數)
 | Do | 升Do | Re | 升Re | Me | Fa | 升Fa | So | 升So | La | 升La | Si
Hz | 270 | 286 | 303 | 321 | 340 | 360 | 382 | 405 | 429 | 454 | 481 | 510
Hz | 540 | 572 | 606 | 642 | 680 | 721 | 764 | 810 | 857 | 908 | 962 | 1019

## Slide 15
(8) Analyzing the Electrocardiogram (ECG)
Is the rhythm of the cardiac valve in synchronization with that of the heart muscle?
Does the heart muscle relax between beats?
From: A. K. Louis, P. Maab, and A. Rieder, “Wavelets Theory and Applications”, John Wiley & Sons, Chichester, 1997.

## Slide 16
(9) 「短期因素」和「長期因素」的分析
economical data
temperature
population
(10) 其他奇奇怪怪的應用
羊毛質料的辦識
指紋的辦識

## Slide 17
Time-frequency Analysis 和Wavelet 在應用上的異同處
相同：都能夠處理一個信號的頻率分佈會隨時間而改變的情形
不同：Time frequency analysis 對於瞬間頻率的分析比較精確
Wavelet 可作「巨觀」和「微觀」的分析
由於 memory requirement 較少，適合 2D 的 image analysis 和 3D 的 video analysis

## Slide 18
附錄十五 希臘字母大小寫與發音一覽表
大寫 | Α | Β | Γ | Δ | Ｅ | Ζ | Η | Θ
小寫 | α | β | γ | δ | ε | ζ | η | θ
英文拚法 | alpha | beta | gamma | delta | epsilon | zeta | eta | theta
KK 音標 | ˋælfə | ˋbetə | ˋgæmə | ˋdɛltə | ˋɛpsələn | ˋzetə | ˋitə | ˋθitə
大寫 | Ι | Κ | Λ | Μ | Ν | Ξ | Ο | Π
小寫 | ι | κ | λ | μ | ν | ξ | ο | π
英文拚法 | iota | kappa | lambda | mu | nu | xi | omicron | pi
KK 音標 | aɪˋotə | ˋkæpə | ˋlæmdə | mju | nu | ksɪ | ˋɑmɪkrɑn | paɪ

## Slide 19
大寫 | Ρ | Σ | Τ | Υ | Φ | Χ | Ψ | Ω
小寫 | ρ | σ | τ | υ | φ,  | χ | ψ | , ω
英文拚法 | rho | sigma | tau | upsilon | phi | chi | psi | omega
KK 音標 | ro | ˋsɪgmə | taʊ | ˋjupsəlɑn | faɪ | kaɪ | saɪ | ˋomɪgə

## Slide 20
附錄十六 Generalization for the Wavelet Transforms
一般的 2-D wavelet transform，其實可分解成沿著 x-axis 以及沿著 y-axis 的 1-D wavelet transforms 的組合
其實，2-D wavelet transform 不一定要沿著 x-axis ， y-axis 來做
Directional 2-D wavelet transforms:
 curvelet
contourlet
bandlet
shearlet
 Fresnelet
 wedgelet
 brushlet
1. Directional Form 2-D Wavelet Transforms

## Slide 21
 Curvelet (ridgelet)
rotation
比較：原本的 1-D wavelet
E. Candès and D. Donoho, "Curvelets – a surprisingly effective nonadaptive representation for objects with edges." In: A. Cohen, C. Rabut and L. Schumaker, Editors, Curves and Surface Fitting: Saint-Malo 1999, Vanderbilt University Press, Nashville (2000), pp. 105–120.

## Slide 22
input
the curvelet transform of the input
results with different 
(four direction for the high-frequency part)

## Slide 23
 Contourlet
M. Do and M. Vetterli, "The contourlet transform: An efficient directional multiresolution image representation," IEEE Trans. Image Processing, vol.14, no.12, pp.2091–2106, Dec. 2005.
masks in the frequency domain
低頻部分 沒有分成不同的方向
高頻部分 分成各種不同的方向

## Slide 24
 Bandlet
根據物體的紋理或邊界，來調整 wavelet transforms 的方向
Stephane Mallet and Gabriel Peyre, "A review of Bandlet methods for geometrical image representation," Numerical Algorithms, Apr. 2002.

## Slide 25
2. Stationary Wavelet Transforms
x[n]
g1[n]
h1[n]
x1,L[n]
g2[n]
h2[n]
x1,H[n]
x2,L[n]
x2,H[n]
g3[n]
h3[n]
x3,L[n]
x3,H[n]
…..
…..
其中
gj[n]
↑2
gj+1[n]
hj[n]
↑2
hj+1[n]
Q: 和原本 discrete wavelet transform 不一樣的地方在哪裡？
G. P. Nason and B. W. Silverman, “The stationary wavelet transform and some statistical applications,” Lecture Notes in Statistics, available in http://citeseerx.ist.psu.edu/viewdoc/download?doi=10.1.1.49.2662&rep=rep1&type=pdf

## Slide 26
3. Bandwidth Form Wavelet Transforms
A little modification for g[n] and h[n]
4. Multi-Band Wavelet Transforms
Instead of only two outputs

## Slide 27
祝各位期末考順利，寒假愉快！
Happy New Year!