## Slide 1
V. Wigner Distribution Function
Definition 1:
Definition 2:
V-A Wigner Distribution Function (WDF)

## Slide 2
Another way for computation
Definition 1:
Definition 2:
where X(f) is the Fourier transform of x(t)
from the frequency domain

## Slide 3
Main Reference
[Ref] S. Qian and D. Chen, Joint Time-Frequency Analysis: Methods and Applications, Chap. 5, Prentice Hall, N.J., 1996.
Other References
[Ref] E. P. Wigner, “On the quantum correlation for thermodynamic equilibrium,” Phys. Rev., vol. 40, pp. 749-759, 1932.
[Ref] T. A. C. M. Classen and W. F. G. Mecklenbrauker, “The Wigner distributionA tool for time-frequency signal analysis; Part I,” Philips J. Res., vol. 35, pp. 217-250, 1980.
[Ref] F. Hlawatsch and G. F. BoudreauxBartels, “Linear and quadratic time-frequency signal representation,” IEEE Signal Processing Magazine, pp. 21-67, Apr. 1992.
[Ref] R. L. Allen and D. W. Mills, Signal Analysis: Time, Frequency, Scale, and Structure, Wiley-Interscience, NJ, 2004.

## Slide 4
The operators that are related to the WDF:
(a) Signal auto-correlation function:
Spectrum auto-correlation function:
(c) Ambiguity function (AF):
Ax(,  )
FTf
FTt
FTf IFTt
Sx(, f )
IFTt
IFTf
Cx(t,  )
Wx(t, f )
x(t)
X(f)

## Slide 5
V-B Why the WDF Has Higher Clarity?
(1) If x(t) = 1
(2) If x(t) = exp(j2 h t)
Comparing: for the case of the STFT
Due to signal auto-correlation function
t
t
f
f

## Slide 6
(3) If x(t) = exp(j2 k t2)
(4) If x(t) = (t)
Page 117
公式(2)
Page 117
公式(5), t0 = 0
t
t
f
f
Page 117
公式(4)
Page 117
公式(2)

## Slide 7
If h(t) =  g(t) +  s(t)
cross terms
V-C The WDF is not a Linear Distribution

## Slide 8
Simulations
x(t) = cos(2t) = 0.5[exp(j2t) + exp(-j2t)]
by the WDF by the Gabor transform
f-axis
f-axis
t-axis
t-axis
1
-1
1
-1
V-D Examples of the WDF

## Slide 9
: rectangular function
by the WDF by the Gabor transform
f-axis
f-axis
t-axis
t-axis

## Slide 10
Gaussian function:
Gaussian function’s T-F area is minimal.
by the WDF by the Gabor transform
f-axis
f-axis
t-axis
t-axis

## Slide 11
for –9  t  1, s(t) = 0 otherwise,
f (t) = s(t) + r(t)
橫軸: t-axis, 縱軸: f -axis
WDF of s(t), WDF of r(t), WDF of s(t) + r(t)

## Slide 12
by the WDF by the Gabor transform
f-axis
f-axis
t-axis
t-axis

## Slide 13
,
(using  = /2 )
Sampling: t = nt, f = mf,  = pt
When x(t) is not a time-limited signal, it is hard to implement.
V-E Digital Implementation of the WDF

## Slide 14
Suppose that x(t) = 0 for t < n1t and t > n2t
x(t)
n1t
n2t
if n + p  [n1, n2]
or n − p  [n1, n2]
 p 的範圍的問題 (當 n 固定時)
n1  n + p  n2 n1 − n  p  n2 − n
n1  n − p  n2 n1 − n  −p  n2 − n, n − n2  p  n − n1
max(n1 − n , n − n2)  p  min(n2 − n , n − n1)
−min(n2 − n , n − n1)  p  min(n2 − n , n − n1)
nt

## Slide 15
x(t)
n1t
n2t
nt
−min(n2 − n , n − n1)  p  min(n2 − n , n − n1)
注意：當 n > n2 或 n < n1 時，
將沒有 p 能滿足上面的不等式
(n2 − n)t , (n − n1 )t : 離兩個邊界的距離
(n − n1)t
(n2 − n )t
−Q
Q

## Slide 16
Q = min(n2n, nn1).
p  [Q, Q], n  [n1, n2],
If x(t) = 0 for t < n1t and t > n2t
possible for implementation
Method 1: Direct Implementation (brute force method)
T點 F點
唯一的限制條件？
(varies with n)

## Slide 17
When and N  2Q+1
Method 2: Using the DFT
q = p+Q → p = q Q
for 0  q  2Q
for 2Q+1  q  N−1
Q = min(n2n, nn1).
n  [n1, n2],
3 大限制條件

## Slide 18
假設 t = n0t, (n0+1) t, (n0+2) t, ……, n1t
f = m0 f, (m0+1) f, (m0+2) f, ……, m1 f
Step 1: Calculate n0, n1, m0, m1, N
Step 2: n = n0
Step 3: Determine Q
Step 4: Determine c1(q)
Step 5: C1(m) = FFT[c1(q)]
Step 6: Convert C1(m) into C( nt, mf)
Step 7: Set n = n+1 and return to Step 3 until n = n1.

## Slide 19
Step 1
Step 2
Step 3
Method 3: Using the Chirp Z Transform

## Slide 20
The computation time of the WDF is more than those of the rec-STFT
and the Gabor transform.
思考：Method 1 的複雜度為多少
思考：Method 2 的複雜度為多少
思考：Method 3 的複雜度為多少

## Slide 21
V-F Properties of the WDF
(1) Projection property | 
(2) Energy preservation property | 
(3) Recovery property | x*(0) 已知
(4) Mean condition frequency and mean condition time | If , then
(5) Moment properties | ,

## Slide 22
(6) Wx(t, f ) is real | 
(7) Region properties | If x(t) = 0 for t > t2 then Wx(t, f ) = 0 for t > t2 If x(t) = 0 for t < t1 then Wx(t, f ) = 0 for t < t1
(8) Multiplication theory | If , then
(9) Convolution theory | If , then
(10) Correlation theory | If , then

## Slide 23
The STFT (including the rec-STFT, the Gabor transform) does not have real region, multiplication, convolution, and correlation properties.
(11) Time-shifting property | If , then
(12) Modulation property | If , then

## Slide 24
 Try to prove of the projection and recovery properties
 Why the WDF is always real?
What are the advantages and disadvantages it causes?

## Slide 25
The importance of region property
 Proof of the region properties
If x(t) = 0 for t < t0,
x(t + /2) = 0 for  < (t0 − t)/2 = −(t − t0)/2,
x(t − /2) = 0 for  > (t − t0)/2,
Therefore, if t − t0 < 0, the nonzero regions of x(t + /2) and x(t − /2) does not overlap and x(t + /2) x*(t − /2) = 0 for all .

## Slide 26
V-G Advantages and Disadvantages of the WDF
Advantages: clarity
many good properties
suitable for analyzing the random process
Disadvantages: cross-term problem
more time for computation, especial for the signal with long time duration
not one-to-one
not suitable for

## Slide 27
V-H Windowed Wigner Distribution Function
When x(t) is not time-limited, its WDF is hard for implementation
with mask
w() is real and time-limited
Advantages: (1) reduce the computation time
(2) may reduce the cross term problem
Disadvantages:

## Slide 28
for p < −Q and p > Q
當然，乘上 mask 之後，有一些數學性質將會消失
Suppose that w(t) = 0 for |t| > B

## Slide 29
(B) Why the cross term problem can be avoided ?
w() is real
Viewing the case where x(t) = (t − t1) + (t − t2)
x(t)
t-axis
t1
t2

## Slide 30
理想情形：
for t  t1, t2
然而，當 mask function w() = 1 時
(也就是沒有使用 mask function)
第一項
第二項
-axis
2t1−2t
2t2−2t
2t−2t2
2t−2t1
-axis
第一項
第二項
from page 117, property 2
Notes: 7

## Slide 31
(3) If t = (t1 + t2)/2
3種情形
(1) If t = t1
(2) If t = t2
第一項
第一項
第一項
第二項
第二項
第二項
-axis
-axis
-axis
-axis
-axis
-axis
2t2−2t1
2t1−2t2
0
0
0
2t1−2t2
0
2t2−2t1
t2−t1
t2−t1
t1−t2
t1−t2
第一項
第二項

## Slide 32
With mask function
Suppose that w() = 0 for || > B, B is positive.
If B < t2 − t1

## Slide 33
(3) t = (t1 + t2)/2
(1) t = t1
(2) t = t2
第一項
第一項
第一項
第二項
第二項
第二項
-axis
-axis
-axis
-axis
-axis
-axis
2t2−2t1
2t1−2t2
0
0
2t1−2t2
0
2t2−2t1
t2−t1
t2−t1
t1−t2
t1−t2
−B
B
B
−B

## Slide 34
附錄五： 研究所學習新知識把握的要點
(1) Concepts: 這個方法的核心概念、基本精神是什麼
(3) Advantages: 這方法的優點是什麼
(4) Disadvantages: 這方法的缺點是什麼
(5) Applications: 這個方法要用來處理什麼問題，有什麼應用
(6) Innovations: 這方法有什麼可以改進的地方
或是可以推廣到什麼地方
(3-1) Why? 造成這些優點的原因是什麼
(4-1) Why? 造成這些缺點的原因是什麼
(2) Comparison: 這方法和其他方法之間，有什麼相同的地方？
有什麼相異的地方

## Slide 35
看過一篇論文或一個章節之後，若能夠回答 (1)-(5) 的問題，就代表你已經學通了這個方法
如果你的目標是發明創造出新的方法，可試著回答 (3-1), (4-1), 和 (6) 的問題