## Slide 1
Applications of Time-Frequency Analysis
for Filter Design
9-1 Signal Decomposition and Filter Design
Signal Decomposition: Decompose a signal into several components.
Filter: Remove the undesired component of a signal
(1) Decomposing in the time domain
t-axis
criterion
component 1
component 2
t0

## Slide 2
(2) Decomposing in the frequency domain
 Sometimes, signal and noise are separable in the time domain  without any transform
 Sometimes, signal and noise are separable in the frequency domain  using the FT (conventional filter)
If signal and noise are not separable in both the time and the frequency domains  (3) Using the fractional Fourier transform and time-frequency analysis
-5 -2 2 5
f-axis

## Slide 3
以時頻分析的觀點，criterion in the time domain 相當於 cutoff line perpendicular to t-axis
以時頻分析的觀點，criterion in the frequency domain 相當於 cutoff line perpendicular to f-axis
t0
=
t-axis
t-axis
f-axis
t0
cutoff line
f0
f-axis
=
f0
t-axis
f-axis
cutoff line

## Slide 4
x(t) = triangular signal + chirp noise 0.3exp[j 0.5(t 4.4)2]
 = -arccot(1/2)
signal + noise
FT
FRFT
reconstructed signal

## Slide 5
x(t) = triangular signal + chirp noise 0.3exp[j 0.5(t 4.4)2]
t-axis
f-axis

## Slide 6
If x(t) = 0 for t < T1 and t > T2
for t < T1 and t > T2 (cutoff lines perpendicular to t-axis)
If X( f ) = FT[x(t)] = 0 for f < F1 and f > F2
for f < F1 and f > F2 (cutoff lines parallel to t-axis)
What are the cutoff lines with other directions?
Decomposing in the time-frequency distribution
with the aid of the FRFT, the LCT, or the Fresnel transform

## Slide 7
 Filter designed by the fractional Fourier transform
means the fractional Fourier transform:
f-axis
Signal
noise
t-axis
FRFT
FRFT
noise
Signal
cutoff line
Signal
cutoff line
noise
比較：


## Slide 8
S(u): Step function
(1)  由 cutoff line 和 f-axis 的夾角決定
(2) u0 等於 cutoff line 距離原點的距離
(注意正負號)

## Slide 9
 Effect of the filter designed by the fractional Fourier transform (FRFT):
Placing a cutoff line in the direction of (sin, cos)
 = 0  = 0.15  = 0.35  = 0.5
(time domain) (FT)

## Slide 10
.
.
t-axis
desired part
undesired part
cutoff line
undesired
part
(t1, 0)
(t0, 0)
cutoff line
f-axis
(0, f1)
 = ? u0 = ?

## Slide 11
  The Fourier transform is suitable to filter out the noise that is a combination of
  sinusoid functions exp(jn1t).
 The fractional Fourier transform (FRFT) is suitable to filter out the noise that
  is a combination of higher order exponential functions
  exp[j(nk tk + nk-1 tk-1 + nk-2 tk-2 + ……. + n2 t2 + n1 t)]
For example: chirp function exp(jn2 t2)
 With the FRFT, many noises that cannot be removed by the FT will be
filtered out successfully.

## Slide 12
(a) Signal s(t) (b) f(t) = s(t) + noise (c) WDF of s(t)
Example (I)

## Slide 13
(d) WDF of f(t) (e) GT of s(t) (f) GT of f(t)
GT: Gabor transform,
WDF: Wigner distribution function
horizontal: t-axis, vertical: -axis

## Slide 14
(g) GWT of f(t) (h) Cutoff lines on GT (i) Cutoff lines on GWT
GWT: Gabor-Wigner transform
根據斜率來決定 FrFT 的 order

## Slide 15
(performing the FRFT)
(j) performing the FRFT
and calculate the GWT
(m) recovered signal (n) recovered signal (green) and the original signal (blue)
(k) High pass filter (l) GWT after filter

## Slide 16
Signal +
(a) Input signal (b) Signal + noise (c) WDF of (b)
(d) Gabor transform of (b) (e) GWT of (b) (f) Recovered signal
Example (II)

## Slide 17
[Important Theory]:
Using the FT can only filter the noises that do not overlap with the signals in the frequency domain (1-D)
In contrast, using the FRFT can filter the noises that do not overlap with the signals on the time-frequency plane (2-D)

## Slide 18
[思考]
Q1: 哪些 time-frequency distribution 比較適合處理 filter 或 signal decomposition 的問題？
Q2: Cutoff lines 有可能是非直線的嗎？

## Slide 19
[Ref] Z. Zalevsky and D. Mendlovic, “Fractional Wiener filter,” Appl. Opt., vol. 35, no. 20, pp. 3930-3936, July 1996.
[Ref] M. A. Kutay, H. M. Ozaktas, O. Arikan, and L. Onural, “Optimal filter in fractional Fourier domains,” IEEE Trans. Signal Processing, vol. 45, no. 5, pp. 1129-1143, May 1997.
[Ref] B. Barshan, M. A. Kutay, H. M. Ozaktas, “Optimal filters with linear canonical transformations,” Opt. Commun., vol. 135, pp. 32-36, 1997.
[Ref] H. M. Ozaktas, Z. Zalevsky, and M. A. Kutay, The Fractional Fourier Transform with Applications in Optics and Signal Processing, New York, John Wiley & Sons, 2000.
[Ref] S. C. Pei and J. J. Ding, “Relations between Gabor transforms and fractional Fourier transforms and their applications for signal processing,” IEEE Trans. Signal Processing, vol. 55, no. 10, pp. 4839-4850, Oct. 2007.

## Slide 20
9-2 TF analysis and Random Process
For a random process x(t), we cannot find the explicit value of x(t). The value of x(t) is expressed as a probability function.
 Auto-covariance function Rx(t, )
(alternative definition of the auto-covariance function:
 Power spectral density (PSD) Sx(t, f )
In usual, we suppose that E[x(t)] = 0 for any t

## Slide 21
Relation between the WDF and the random process
Relation between the ambiguity function and the random process

## Slide 22
 Stationary random process:
the statistical properties do not change with t.
Auto-covariance function
for any t,
PSD:
White noise: where  is some constant.

## Slide 23
 When x(t) is stationary,
(invariant with t)
(nonzero only when  = 0)
a typical E[Wx(t, f)] for stationary random process
a typical E[Ax(, )] for stationary random process
t
f
η
τ

## Slide 24
[Ref 1] W. Martin, “Time-frequency analysis of random signals”, ICASSP’82, pp. 1325-1328, 1982.
[Ref 2] W. Martin and P. Flandrin, “Wigner-Ville spectrum analysis of nonstationary processed”, IEEE Trans. ASSP, vol. 33, no. 6, pp. 1461-1470, Dec. 1983.
[Ref 3] P. Flandrin, “A time-frequency formulation of optimum detection” , IEEE Trans. ASSP, vol. 36, pp. 1377-1384, 1988.
[Ref 4] S. C. Pei and J. J. Ding, “Fractional Fourier transform, Wigner distribution, and filter design for stationary and nonstationary random processes,” IEEE Trans. Signal Processing, vol. 58, no. 8, pp. 4079-4092, Aug. 2010.
 For white noise,

## Slide 25
Filter Design for White noise
conventional filter
by TF analysis
Signal
t-axis
f-axis
white noise everywhere
Ex: energy of the signal
A: area of the time frequency distribution of the signal
The PSD of the white noise is Sn(f) = 

## Slide 26
If varies with t and is nonzero when   0,
then x(t) is a non-stationary random process.
If 
 xn(t)’s have zero mean for all t’s
 xn(t)’s are mutually independent for all t’s and ’s
if m  n, then ,

## Slide 27
(1) Random process for the STFT
E[x(t)]  0 should be satisfied.
Otherwise,
for zero-mean random process, E[X(t, f )] = 0
(2) Decompose by the AF and the FRFT
Any non-stationary random process can be expressed as a summation of the fractional Fourier transform (or chirp multiplication) of stationary random process.

## Slide 28
-axis
-axis
An ambiguity function plane can be viewed as a combination of infinite number of radial lines.
Each radial line can be viewed as the fractional Fourier transform of a stationary random process.

## Slide 29
信號處理小常識
white noise
α ≠ 0 color noise

## Slide 30
附錄九 Time-Frequency Analysis 理論發展年表
AD 1785 The Laplace transform was invented
AD 1812 The Fourier transform was invented
AD 1822 The work of the Fourier transform was published
AD 1910 The Haar Transform was proposed
AD 1927 Heisenberg discovered the uncertainty principle
AD 1929 The fractional Fourier transform was invented by Wiener
AD 1932 The Wigner distribution function was proposed
AD 1946 The short-time Fourier transform and the Gabor transform was proposed.
In the same year, the computer was invented
AD 1961 Slepian and Pollak found the prolate spheroidal wave function
AD 1965 The Cooley-Tukey algorithm (FFT) was developed
註：沒列出發明者的，指的是 transform / distribution 的名稱和發明者的名字相同

## Slide 31
AD 1966 Cohen’s class distribution was invented
AD 1970s VLSI was developed
AD 1971 Moshinsky and Quesne proposed the linear canonical transform
AD 1980 The fractional Fourier transform was re-invented by Namias
AD 1981 Morlet proposed the wavelet transform
AD 1982 The relations between the random process and the Wigner distribution function was found by Martin and Flandrin
AD 1988 Mallat and Meyer proposed the multiresolution structure of the wavelet transform;
In the same year, Daubechies proposed the compact support orthogonal wavelet
AD 1989 The Choi-Williams distribution was proposed; In the same year, Mallat proposed the fast wavelet transform
註：沒列出發明者的，指的是 transform / distribution 的名稱和發明者的名字相同

## Slide 32
AD 1990 The cone-Shape distribution was proposed by Zhao, Atlas, and Marks
AD 1990s The discrete wavelet transform was widely used in image processing
AD 1993 Mallat and Zhang proposed the matching pursuit;
In the same year, the rotation relation between the WDF and the fractional Fourier transform was found by Lohmann
AD 1994 The applications of the fractional Fourier transform in signal processing were found by Almeida, Ozaktas, Wolf, Lohmann, and Pei;
Boashash and O’Shea developed polynomial Wigner-Ville distributions
AD 1995 Auger and Flandrin proposed time-frequency reassignment
L. J. Stankovic, S. Stankovic, and Fakultet proposed the pseudo Wigner distribution
AD 1996 Stockwell, Mansinha, and Lowe proposed the S transform
Daubechies and Maes proposed the synchrosqueezing transform.
AD 1998 N. E. Huang proposed the Hilbert-Huang transform
Chen, Donoho, and Saunders proposed the basis pursuit

## Slide 33
AD 1999 Bultan proposed the four-parameter atom (i.e., the chirplet)
AD 2000 The standard of JPEG 2000 was published by ISO
Another wavelet-based compression algorithm, SPIHT, was proposed by Kim, Xiong, and Pearlman
The curvelet was developed by Donoho and Candes
AD 2000s The applications of the Hilbert Huang transform in signal processing, climate analysis, geology, economics, and speech were developed
AD 2002 The bandlet was developed by Mallet and Peyre;
Stankovic proposed the time frequency distribution with complex arguments
AD 2003 Pinnegar and Mansinha proposed the general form of the S transform
Liebling et al. proposed the Fresnel.
AD 2005 The contourlet was developed by Do and Vetterli;
The shearlet was developed by Kutyniok and Labate
The generalized spectrogram was proposed by Boggiatto, et al.

## Slide 34
時頻分析理論未來的發展，還看各位同學們大顯身手
AD 2006 Donoho proposed compressive sensing
AD 2006~ Accelerometer signal analysis becomes a new application.
AD 2007 The Gabor-Wigner transform was proposed by Pei and Ding
AD 2007~ Many theories about compressive sensing were developed by Donoho, Candes, Tao, Zhang ….
AD 2010~ Many applications about compressive sensing are found.
AD 2012 The generalized synchrosqueezing transform was proposed by Li and Liang
AD 2015~ Time-frequency analysis was widely combined with the deep learning technique for signal identification
AD 2017 The wavelet convolutional neural network was proposed by Kang et al.
The higher order synchrosqueezing transform was proposed by Pham and Meignen
AD 2018~ With the fast development of hardware and software, the time- frequency distribution of a 106-point data can be analyzed efficiently within 0.1 Second