## Slide 1
Homework 2 (Due: 12th Nov.)
(1) Why it is proper to choose a large  for the scaled Gabor transform with window  1/4exp(-2) in music signal analysis ? (10 scores)
(2) What are the main advantage (write one term) and the main disadvantages (write three terms) of the recursive method for STFT implementation?
(10 scores)
(3) What are the two conditions that the WDF may have the cross term problem?
(10 scores)
(4) Calculate the WDFs of (a) cos(2πt), (b) sin2(2πt). (15 scores)
(5) (a) Why the windowed WDF requires less computation time? (b) In what conditions that the windowed WDF can avoid the cross term problem? (10 scores)
(6) In what condition the output of Cohen’s class distribution is real? (Written the constraint for (, )) (10 scores)

## Slide 2
Example：
dt=0.05; df=0.05;
t1=[0:dt:10-dt]; t2=[10:dt:20-dt]; t3=[20:dt:30];
t=[0:dt:30];
f=[-5:df:5];
x=[cos(2*pi*t1),cos(6*pi*t2),cos(4*pi*t3)];
tic
y=recSTFT(x, t, f);
toc
(i) The code should be handed out by ceiba
(ii) Choose an input x. Plot the output y.
(iii) Use tic and toc to determine the running time
(iv) Write by the FFT-based method
(7) Write a Matlab or Python program for the rectangular STFT. (35 scores) (the window is w(t) = 1 if |t| < B, w(t) = 0 otherwise).
y = recSTFT(x, t, f, B)
x: input, t: samples on t-axis, f: samples on f-axis, y: output
(Extra): Answer the questions according to your student ID number.
(ended with 0, 3, 4, 5, 8, 9)