## Slide 1
(1) Write a Matlab (or Python) program for the scaled Gabor transform (unbalanced form).
y = Gabor(x, tau, t, f, sgm) (35 scores)
x: input, tau: samples on t-axis for the input, t: samples on t-axis for the output
f: samples on f-axis, sgm: scaling parameter, y: output
(i) The code should be hauded out by ceiba, (ii) Write as a function ，(iii) Choose an input x (Use *.wav)， plot the output y ， (iv) Use tic and toc to show the running time，(v) The running time should be as short as possible (for the following example, within 1.5 seconds)
[a1, fs] = audioread('Chord.wav');
x=a1(:,1).‘; % only extract the first channel
tau = (? Please think how to determine tau);
dt = 0.01; df= 1;
sgm= 200;
t= 0:dt:max(tau); f= 20:df:1000;
tic
y= Gabor (x, tau, t, f, sgm);
toc
Homework 3 (Due: Dec. 3rd)

## Slide 2
(2) Why the following transforms can avoid the cross term? (a) Cohen’s class distribution; (b) the Gabor-Wigner transform. (10 scores)
(3) Why can we get a clear time-frequency distribution by (a) the generalized spectrogram; (b) time-frequency reassignment? (10 scores)
(4) When we apply the polynomial WDF with q = 6, for which of the following functions the cross term still exists? Why?
(5) exp(j(t3+t)); (b) exp(jt5); (c) exp(-t2/10); (d) cos(t3). (10 scores)
(6) Suppose that the WDFs of x(t) and exp(j(at3+bt2+ct))x(dt +e) are the left and the right figures, respectively. Determine the values of a, b, c, d , e. (15 scores)
(3,4)
(3,2)
(-3,2)
(-3,4)
parabola
(0,0)
(3,0)
(0,2)
(0,-2)

## Slide 3
(7) (a) How do we use the fractional Fourier transform to generate the following four cutoff lines on the time-frequency distribution? (10 scores)
– t + f < 6, -12 < 2t + f < 6, and 4t – f <12.
(b) How do we generate the cutoff line of 2 + 2t2 + t4 > f > 2t2 + t4 ?
(5 scores)
(c) Can we use the LCT to generate a tilted cutoff time in the time-frequency distribution ? Why? (5 scores)
(Extra): Answer the questions according to your student ID number.
(ended with 1, 2, 3, 6, 7, 8)